PROFESSIONAL CALIBRATION

CHECK LIST

Pro_cklst.doc       07/99     rev 6

The POST INSTALLATION and HANGAR CALIBRA-TION check lists must be completed prior to flight.  The zero “G” maneuver requires that all unsecured items be removed from the aircraft prior to flight.  Two pilots are required during the calibration process and one will be assigned the task to fly the aircraft and nothing more.  The flight calibration area will be cleared for traffic and will be at a safe altitude with the IAS always within the green IAS band.  Stalls are not required or desired!

Prior to the in flight calibration and to eliminate the possible false "angle angle push" warnings pull the AOA circuit breaker.

POST INSTALLATION PRE FLIGHT

Blow into Blue tube at CPU	Air exits Upper Wing Port

Blow into Green tube at CPU	Air exits lower Wing Port

Blow into Red tube at the CPU	IAS increases

Suck on Clear tube at the CPU	Altimeter increases

PITOT/STATIC LEAK TEST	COMPLETED

AIRCRAFT LOG	UPDATED

AIRCRAFT CHECKLISTS	UPDATED

ANNUAL CONDITION C/L	UPDATED

CHAPTER IX TESTING	COMPLETED

HANGAR CALIBRATION

AIRCRAFT LOCATION	HANGAR

CALIBRATION WAND	INSTALLED

GEAR SWITCH	DOWN

AOA POWER	ON

AOA SELF TEST	PASSED or ERRORS

AUDIO VOLUME	ADJUSTED

FLAPS UP	DONUT CHECKED OFF

FLAPS DOWN	DONUT CHECKED ON

MODE SWITCH	PUSH/RELEASE

PAGE  flap down hangar calibrate	1HC

RECORD SWITCH	PUSH/RELEASE

MODE SWITCH	4x PUSH/RELEASE

PAGE  landing gear extend	1LE

RECORD SWITCH	PUSH/RELEASE

PAGE  save data to non-volatile memory	1SA

RECORD SWITCH	PUSH/RELEASE

AOA POWER	OFF

FLY THE AIRPLANE

and

watch for traffic

CRUISE CONFIGURATION

CALIBRATION

AIRCRAFT LOCATION	AIRBORNE

AOA POWER ON	ERRORS 11, 12 & 33

FLAPS/GEAR	 CONFIRMED UP

MODE SWITCH	2x PUSH/RELEASE

PAGE  flaps up zero lift	0OL

ZERO “G” MANEUVER for 1/2 sec.	YES

RECORD SWITCH	PUSH/RELEASE

PAGE  flaps up angle advisory	0AA

SLOW FLIGHT IAS descending flight	1.15xVs1

RECORD SWITCH	PUSH/RELEASE

MODE SWITCH	3x PUSH/RELEASE

PAGE  save flaps up data to non-volatile memory	0SA

RECORD SWITCH	PUSH/RELEASE

LANDING CONFIGURATION

CALIBRATION

AIRCRAFT LOCATION	AIRBORNE

FLAPS/GEAR	CONFIRMED DOWN

MODE SWITCH	2x PUSH/RELEASE

PAGE  flaps down zero lift	1OL

ZERO “G” MANEUVER for 1/2 sec.	YES

RECORD SWITCH	PUSH/RELEASE

PAGE  flaps down angel advisory	1AA

SLOW FLIGHT IAS descending flight	1.15xVso

RECORD SWITCH	PUSH/RELEASE

MODE SWITCH	3x PUSH/RELEASE

PAGE  save flaps down data to non-volatile memory	1SA

RECORD SWITCH	PUSH/RELEASE

GEAR WARNING CALIBRATION

AIRCRAFT LOCATION	AIRBORNE

FLAPS	 CONFIRMED DOWN

GEAR	UP

MODE SWITCH	6x PUSH/RELEASE

PAGE  flaps down Landing gear extend	1LE

AIRSPEED approach + 15 knots	YES

RECORD SWITCH	PUSH/RELEASE

PAGE  save flaps down data to non-volatile memory	1SA

RECORD SWITCH	PUSH/RELEASE

FLAPS	CONFIRMED UP

MODE SWITCH	7x PUSH/RELEASE

PAGE  save flaps up data to non-volatile memory	0SA

RECORD SWITCH	PUSH/RELEASE

FLIGHT TEST AOA

CHAPTER X CALIBRATING	COMPLETE

CHAPTER X FLIGHT TESTING 	COMPLETE

CALIBRATION WAND	RETURN to PSS, Inc.